## Slide 1: Architecting Programmable Data Plane Defenses into the Network with FastFlex
Jiarong Xing, Wenqing Wu, Ang Chen
Rice University

## Slide 2
Motivation: Mitigating network attacks
Attacks are increasing and they are getting more advanced
  Needle-in-a-haystack attacks (e.g., data exfiltration)
  Volumetric attacks (e.g., DDoS)
  Dynamic changing attacks (e.g., Link-flooding)
  …
We need programmable defenses!
Amazon.com goes down, loses $66,240 per minute
'Internet Of Things' hacking attack led to widespread outage of popular websites
Hacked home devices caused massive Internet outage
Power grid cyber attacks keep the Pentagon up at night
Cyberattacks: Stuxnet and Flame
Internet shutdowns cost countries $2.4 billion last year
Global DNS outage
hits Microsoft Azure customers
The world’s largest DDoS attack took GitHub offline for fewer than 10 minutes
Equifax is still paying for its data breach: $1.4 billion and counting
Incapsula estimates DDoS attacks cost $40,000 per hour

## Slide 3
State of the art: OpenFlow-based SDN defenses
Defense apps run on the central controller.
Switches send sampled traffic to the controller.
The controller makes defense decisions.
SDN switch
SDN switch
SDN controller
Aggregate/Sampled data
Responses
SPIFFY(NDSS’16)
PBS(NDSS’16)
…
vNIDS(CCS’18)

## Slide 4
Limitations of OpenFlow-based SDN defenses
Can only handle sampled traffic
  May miss needle-in-a-haystack attacks
Make decisions with high latency
  Would fall behind of fast dynamic changing attacks
The central controller might become the bottleneck
  Vulnerable to saturation attacks (e.g. Avant-guard CCS’13)
Key reason: Can only program the central controller

## Slide 5
New opportunity: Programmable data planes
Memory
ALU
Match/
Action
Table
Match/
Action
Table
Match/
Action
Table
Programmable
Parser
Programmable
Deparser
Switch control plane
PCIe bus
Stages
Stages
Programmable data planes
  Can be programmed in high-level languages (e.g., P4)
  Customized protocols, persistent state, custom match/actions
  All at linespeed (Tbps)!

## Slide 6
Per-packet visibility
  Can detect needle-in-a-haystack attacks
Per-packet dynamicity
  Can respond as fast as dynamic changing attacks
Scale-free defense
  Naturally scales with network size and speed
This is great news for security!
  Three key
  advantages

## Slide 7
Vision: Programmable in-network security
Programmable In-network security:
  Deploys a wide range of defenses in-network
  Synchronizes them for whole-network defense!
Simultaneous routing and security!
We believe this is achievable in two steps

## Slide 8
Vision: A switch is a defense platform
Runs a wide range of security apps
Dynamically swaps in the right app as it forwards traffic.
Security ”apps”
Work: NetHide (USENIX Security’18), Heavy Hitter Detection (SOSR’18), Poise (USENIX Security’20), …

## Slide 9
Architect a wide range of defenses into network paths
Networks mitigate attacks as they route traffic
Vision: A network is a defense fleet
A
C
D
E
F
B
Focus of FastFlex

## Slide 10
Approach: FastFlex
(b) Generate optimal deployment
(c) Distributed control
Joint analysis of all apps

## Slide 11
Outline
Motivation: Mitigating network attacks
State of the art: SDN defenses
Approach: FastFlex
  Resource multiplexing
  Optimal placements
  Distributed control
  Dynamic scaling
Case study: Link-flooding attacks

## Slide 12
Challenge #1: Resource multiplexing
Security ”apps”
  Problem:
    How to deploy multiple applications in a single switch?
    How to deploy a large application in a single switch?

## Slide 13
Solution: Program decomposition + sharing
A
B
F
E
C
D
P4 programs
Data flow graphs
  Smaller components are easier to pack than larger ones.
  Component sharing improves resource utilization.
A
C
G
E
A
B
F
E
C
D
+
A
B
F
E
C
D
G
Data flow graph
Full data flow graph

## Slide 14
Challenge #2: Defense placement
  Problem: How to find an optimal deployment for a network?

## Slide 15
Opportunity: Pervasive distribution
  Existing methods in placing middleboxes, e.g. FlowTags (NSDI’14), etc.
  Key difference: Pervasive distribution
    Reduces traffic detour
    Prevents hotspots from forming
A
B
F
E
C
D
G
Network topology
+
Network deployment
Full data flow graph
A
C
B
E
G
F
D
B

## Slide 16
Challenge #3: Distributed control
Problem: How to synchronize switches entirely in the data plane?
SDN switch
SDN controller
SDN switch

## Slide 17
Solution: Distributed data plane probes
  Using data plane probes to communicate with other switches
P4 switch
P4 switch

## Slide 18
Challenge #4: Unpredictable attack patterns
Problem: How to handle unpredictable attacks patterns?
A
B
C
B
E
G
F
D

## Slide 19
Solution: Dynamic scaling
  Dynamic scaling up and down
  State migration across switches
  Handling fault tolerance, e.g. forward error correction
  Updating routing rules of upstream switches
A
B
C
B
E
G
F
D
A
B
C
G
F
D
E
E
B

## Slide 20
Outline
Motivation: Mitigating network attacks
State of the art: SDN defenses
Approach: FastFlex
  Resource multiplexing
  Optimal placements
  Distributed control
  Dynamic scaling
Case study: Link-flooding attacks

## Slide 21
Case study: Link-flooding defense
Can congest critical links to cut off victims from the network.
Can dynamically change target links

## Slide 22
State-of-the-art: Traffic rerouting with SDNs
Find alternative routes by the central controller, e.g. SPIFFY(NDSS’16).
Reroute traffic to alleviate congestion on the target link.
SDN controller

## Slide 23
Our defense: Traffic rerouting with FastFlex
Find alternative routes by probes on data plane in a distributed manner.
See more defenses in our paper!

## Slide 24
Experimental setup
Proof-of-concept prototype:
  Runs in ns3 + P4 bmv2.
Scenario:
  Two critical links in the topology
  The attacker dynamically changes her target links.
Baseline:
  An SDN-based defense that performs centralized TE to reconfigure the network. (SPIFFY, NDSS’16)

## Slide 25
FastFlex mitigates link-flooding attacks effectively
The SDN defense: Constantly falls behind.
FastFlex: Disperses the traffic almost instantaneously.
Time (seconds)
Normalized throughput

## Slide 26
Summary
Motivation: Mitigating network attacks
Opportunity: Programmable data planes
Three key advantages:
  Per-packet visibility
  Per-packet dynamicity
  Scale free defense
Vision: Programmable in-network security
  A switch as a defense platform
  A network as a defense fleet
Thanks!