## Slide 1: NetWarden: Mitigating Network Covert Channels without Performance Loss
Jiarong Xing, Adam Morrison, Ang Chen
Rice University

## Slide 2
Motivation: Mitigating network covert channels
Secretary
President
Launch code:
1011
Code is 1011
Ah! 1011
Attacker
Launch code
Covert channels:
TCP hdr: 1011
H E L L O
H
E
L
L
O
1
0
1
1
  Storage channels: changing the packet header fields.
  Timing channels: changing the timing of packets.

## Slide 3
State of the art: Existing channels
Covert storage channels:
  TCP initial sequence number channel (Rowland, 1997)
  IP TTL channel (Qu, 2004)
  Partial ACK channel (Luo, 2009)
  …
Covert timing channels:
  IP timing channel (Cabuk, 2004)
  TCP timing channel (Luo, 2008)
  Physical layer channel (Lee, 2014)
  …
Covert channels can leak data over long distance effectively
“Common Criteria” require protection against both channel types!

## Slide 4
State of the art: Storage channel defense
replace (+2)
Repeat for EVERY packets for Tbps traffic
Field X = a
replace (+2)
Field X = a +2
Field X = b
replace (+2)
Field X = b +2
Field X = c
replace (+2)
Field X = c +2
Field X = d
replace (+2)
Field X = d +2
…
State-of-the-art solutions are software-based
  Detection: Per-packet header inspection
  Mitigation: Per-packet header modification
TCP sender
TCP hdr: 1011
H E L L O
TCP receiver
TCP hdr: 1101
H E L L O
As a result, they are very inefficient!

## Slide 5
State of the art: Timing channel detection
Detection: Statistics-based tests over packet gaps
  Looking for signs of statistical deviation
   Not always accurate
H
E
L
L
O
Normal traffic:
H
E
L
L
O
With channel:
Two peaks
One peak
Distribution of packet gaps
1
0
1
1

## Slide 6
With channel:
After mitigating:
H
E
L
L
O
1
0
1
1
H
E
L
L
O
1
1
1
0
extra delay
State of the art: Timing channel mitigation
Mitigation: Add random delay to each packet
  Destroy the original timing of the packets
It will increase the latency of TCP connections

## Slide 7
Problem: Performance penalty
Detection:
  Per-packet inspection required
  Software cannot keep up with Tbps traffic
Mitigation:
  Adding random delay to each packet  Increase latency
  Collateral damage  Affects legitimate traffic (e.g., false positives)

## Slide 8
Key question
Can we mitigate covert channels
while preserving performance?

## Slide 9
Approach: NetWarden
    NetWarden: A performance-preserving covert channel defense.
Secretary
President
Launch code:
1011
????
Attacker
TCP hdr: 1011
H E L L O
H
E
L
L
O
1
0
1
1
ToR switch
NetWarden

## Slide 10
Key challenges and solutions
      Challenge #1: Efficient detection
        Solution: Use programmable switches
      Challenge #2: Performance-preserving mitigation
        Solution: Performance “boosting”
      Challenge #3: Hardware limitations
        Solution: Fastpath/slowpath co-design

## Slide 11
Outline
Motivation: Mitigating network covert channels
State of the art: Performance penalty
Approach: NetWarden
NetWarden design
  Challenge #1: Efficient detection
  Challenge #2: Performance-preserving mitigation
  Challenge #3: Hardware limitations
Initial validation
Ongoing work
Conclusion

## Slide 12
Challenge #1: Efficient detection
Solution: Detecting covert channels on programmable switches.
Problem: Software-based detection cannot handle Tbps traffic.
Programmable switches have two layers:
  Control plane: General purpose CPU.
  Data plane: Programmable ASIC.
Memory
Switch control plane
Memory
Memory
Memory

## Slide 13
Challenge #2: Performance-preserving mitigation
Two boosters:
  ACK booster: Generate ACK packets in advance.
  Receive window booster: Enlarge receive window field temporarily.
Solution: Temporarily boosting TCP performance to neutralize the performance penalty.
Two boosters:
  ACK booster: Generate ACK packets in advance.
  Receive window booster: Enlarge receive window field temporarily.
Problem: Existing mitigations incur performance loss.

## Slide 14
Boosting performance: ACK booster
data1
ACK1
NetWarden
data1
data2
ACK1
data2
Performance boosting
Creates the illusion of a shorter latency as perceived by the sender.

## Slide 15
Challenge #3: Hardware limitations
Solution: Fastpath/slowpath co-design
Problem: The data plane has hardware restrictions
  E.g., does not support packet caching
  Or complex statistical tests
Packet buffers
Statistical tests
Traffic
Fast path
(data plane)
Slow path
(control plane)
Storage channel detector
Timing channel detector

## Slide 16
Outline
Motivation: Mitigating network covert channels
State of the art: Performance penalty
Approach: NetWarden
NetWarden design
  Challenge #1: Efficient detection
  Challenge #2: Performance-preserving mitigation
  Challenge #3: Hardware limitations
Initial validation
Ongoing work
Conclusion

## Slide 17
Experimental setup
Proof-of-concept prototype:
  P4 for fastpath
  Python for slowpath
  Runs in software-based simulator.
Two covert channels:
  Channel #1: TCP storage channel
  Channel #2: IP timing channel
Scenario: Client downloads file from NetWarden-protected server
Baseline: A naïve defense without performance boosting

## Slide 18
Results: Effectiveness
NetWarden can mitigate covert channels effectively.
Bit decoding error rate (%)
100
75
50
25
0
4
50
No defense Naïve defense NetWarden
49
Random guess
Perfect decoding
Perfect decoding (flip 0/1)
Naïve defense: renders decoding to a random guess.
NetWarden: very close to a random guess.

## Slide 19
Results: Performance
NetWarden can mitigate covert channels with minimal performance loss.
Normalized file downloading time
1.2
1.1
1.0
0.9
1.00
1.18
No defense Naïve defense NetWarden
1.03
Naïve defense incurs 18% extra downloading time.
NetWarden only incurs 3% extra downloading time.

## Slide 20
Ongoing work
How should we divide the labor between fastpath and slowpath?
  “Optimal” division of labor
How much performance boosting should NetWarden perform?
  Too much  unfair to other connections
  Too little  cannot neutralize performance loss
How can we make NetWarden effective for all TCP variants?

## Slide 21
Conclusion
Motivation: Mitigating network covert channels
Key limitation of existing approaches:
  Performance penalty
Our approach: NetWarden
  Using programmable data planes
  Performance boosting
  Fastpath/slowpath design
The goal of NetWarden:
  Mitigating covert channels without performance loss!
Questions?