## Slide 1: NetWarden: Mitigating Network Covert Channels while Preserving Performance
Jiarong Xing, Qiao Kang, Ang Chen
Rice University

## Slide 2
Motivation: Mitigating network covert channels
Secretary
President
Launch code:
1011
Code is 1011
Ah! 1011
Attacker
Launch code
Covert channels:
TCP hdr: 1011
H E L L O
H
E
L
L
O
1
0
1
1
  Storage channels: changing the packet header fields.
  Timing channels: changing the timing of packets.

## Slide 3
Covert channels are a difficult problem
Detection is difficult due to non-determinism
  Protocols fields, e.g., TCP initial sequence numbers
  Protocol events, e.g., inter-packet gaps
Mitigation is difficult due to high traffic volume
  Operate on every packet of Tbps traffic
TCP ISN: 1011
H E L L O
A malicious packet
A normal packet
H
E
L
L
O
Malicious timing
Normal timing

## Slide 4
State of the art
replace (+2)
SeqNo = a
replace (+2)
SeqNo = a +2
SeqNo = b
replace (+2)
SeqNo = b +2
SeqNo = c
replace (+2)
SeqNo = c +2
SeqNo = d
replace (+2)
SeqNo = d +2
…
Many defenses have been proposed:
  ISN storage channel:
    Add the same offset to TCP sequence numbers
  IP timing channel:
    Add random delays to destroy original timing
TCP sender
TCP ISN: 1011
H E L L O
With channel:
After mitigating:
H
E
L
L
O
1
0
1
1
H
E
L
L
O
1
1
1
0
TCP sender
TCP ISN: 1101
H E L L O

## Slide 5
Common problem: Performance penalty
Per-packet operation running in software is very inefficient
  Switches have to handle Tbps traffic
Incur extra delay to TCP connections
  Many flows are delay sensitive
Not practical for deployment!

## Slide 6
Key question
Can we mitigate covert channels
while preserving performance?

## Slide 7
New opportunity: Programmable switches
Memory
ALU
Match/
Action
Table
Match/
Action
Table
Match/
Action
Table
Programmable
Parser
Programmable
Deparser
Switch control plane
PCIe bus
Stages
Stages
Programmable switches
  Can be programmed in high-level languages (e.g., P4)
  Run at linespeed (Tbps)
  Widely used in network community:
    SilkRoad-Sigcomm’17, Speedlight-Sigcomm’18, Blink-NSDI’19, Contra-NSDI’20, etc.
An ideal candidate for covert channel defenses!

## Slide 8
NetWarden: A programmable switch defense
NetWarden mitigates covert channels while preserving performance.
Covert channels
Normal traffic
NetWarden
A programmable switch

## Slide 9
Key features
NetWarden
Effective defenses
Defend against a wide range
of covert channels
High throughput
~100Gbps per switch port
Performance preservation
Great transparency
< 1% performance deviation
Totally transparent to end hosts

## Slide 10
Outline
Motivation: Mitigating network covert channels
State of the art: Performance penalty
Approach: NetWarden
NetWarden design
  Challenge #1: Limited programming model
  Challenge #2: Performance preservation
Evaluation
Conclusion

## Slide 11
      Solution: hardware/software co-design principle.
Challenge #1: Limited programming model

## Slide 12
Memory
ALU
Match/
Action
Table
Match/
Action
Table
Match/
Action
Table
Switch control plane
PCIe bus
Stages
Stages
Data plane
  Header modification, ns timestamp, per-flow state, line speed
  Limited memory, limited arithmetic computation
Control plane
  Abundant memory, complex arithmetic computation
  Software speed
Complementary!
Programmable switch anatomy

## Slide 13
Applying the hardware/software co-design principle
Switch data plane
Switch control plane
Computation: Per-packet operations
Memory: Constant state
Computation: Batch operations
Memory: Growing state
Minimize crosstalk

## Slide 14
Applying the hardware/software co-design principle
Switch data plane
Switch control plane
Statistical tests
Packet caching
RTT
measurement
IPD
maintenance
Header
modification
Per-flow state
maintenance

## Slide 15
Challenge #2: Performance preservation
Problem: Existing mitigations incur performance loss.
Takeaway: Create the illusion of the same RTT for the sender.
Extra delay
data
ACK
data
ACK
data
data
data
ACK
ACK

## Slide 16
Solution: Performance boosters
ACK booster
Receiving window booster
  ACK booster
    Maintain the same RTT by generating ACK packets in advance.
  Receiving window booster
    Send more data per RTT by enlarging the receiving window size.

## Slide 17
Performance preservation: ACK booster
NetWarden
Creates the illusion of the same RTT as perceived by the sender.
Retransmission
①
②
③
④
⑤

## Slide 18
Outline
Motivation: Mitigating network covert channels
State of the art: Performance penalty
Approach: NetWarden
NetWarden design
  Challenge #1: Limited programming model
  Challenge #2: Performance preservation
Evaluation
Conclusion

## Slide 19
Evaluation setup
NetWarden prototype:
  Runs in Tofino Wedge 100BF-32X switch.
  2500 LoC of P4 + 3000 LoC of C+Python
Threat model:
  A compromised server + a trusted P4 switch running NetWarden
  Leak a 2048-bit RSA key via covert channel.
Real world applications:
  Apache servers, FTP servers, Nodejs servers
Baseline:
  No defense: No covert channel defenses are deployed.
  Naïve defense: Covert channel defenses without performance preservation

## Slide 20
How effective is NetWarden in covert channels mitigation ?
NetWarden can mitigate covert channels effectively.
Naïve defense: renders decoding to a random guess.
NetWarden: very close to a random guess.

## Slide 21
NetWarden can mitigate covert channels with minimal performance loss.
Naïve defense incurs 25% performance penalty.
NetWarden only has 1% performance deviation.
How well does NetWarden preserve performance?
No defense
Naive
No defense
NetWarden
Naive

## Slide 22
See more evaluation results in our paper
Different TCP variants
System scalability
System overhead
Complex Applications
Self-defense techniques

## Slide 23
Outline
Motivation: Mitigating network covert channels
State of the art: Performance penalty
Approach: NetWarden
NetWarden design
  Challenge #1: Limited programming model
  Challenge #2: Performance preservation
Evaluation
Conclusion

## Slide 24
Conclusion
Motivation: Mitigating network covert channels
Key limitation of existing approaches:
  Performance penalty
Our approach: NetWarden
  Principles of hardware/software co-design
  Efficient defenses
  Performance preservation
Evaluation:
  Mitigates covert channels with minimum performance loss!
Source code: https://github.com/jiarong0907/NetWarden
Looking for internship in 2021 summer!
Questions?